Antennas, December 2002

FITTING PL259 PLUGS

As part of the coax cable reorganisation described above I had to fit PL259 plugs to the RG-213 cable. I find the recommended way of doing this a pig of a job. Yes, I know that it is, or was, the standard soldering exercise for novices so I can only conclude my soldering abilities are below par.  I can never be sure if I have used enough heat to make the solder run through the holes to make a good dry joint free connection to the braid, or I have seriously cooked the coax. Trying to reclaim such a soldered plug is a messy business. Greg Ordy, W8WWW, claims that a blow torch is better for the job although this is only part of the story, (Go to Google Advanced Search and type in 'PL-259 plugs'.)

My solution is to make up the end of the cable as recommended but make a loose pigtail of the braid and fold it back over the coax sheath. The cable is then screwed into the into the plug and centre connection soldered. The protruding braid is then cropped so that there is approximately 5mm folded back over the body of the plug.  The braid can be soldered to the plug, a much easier task than soldering through the holes, and the soldered joint can be inspected for a good solder flow.

PL259 plugs are occasionally available with clamp nuts and pressure sleeves (as fitted to N-type plugs), which is a much better solution.

Antennas, March 2003

FITTING PL259 PLUGS

In the December edition of Antennas I said that I found the recommended way of fixing PL529 connectors to coaxial cable difficult and less than reliable. The reason being that you can never be sure if enough heat has been used make the solder run through the holes to make a good dry joint free connection to the braid without cooking the coax insulation.

The problem was further brought home when I tried to locate the fault on one of the VHF antenna feeders at GB2CPM. The symptom was an open feeder and the fault was eventually found to be at the shack end. All the connectors in the line are N-type with clamp nuts pressure sleeves; with the exception of the one in the shack, which used a solder type connection.

The connector and a short length of feeder were cropped off and a new plug fitted. The old plug was disassembled, as shown in Fig 1, to find out what had gone wrong. The cable had been made up perfectly with 1/4in (6mm) of braiding neatly trimmed and tinned. The prepared end had been screwed into the plug and the centre and braid soldered to in the appropriate manner.  In all probability the cable would have passed an initial continuity test; however although the centre pin was soldered correctly the braid was not. Over a period of time a layer of corrosion had caused the braid/plug connection to become open circuit. It was for that reason that in December Antennas I proposed a solution of fixing the coax braid to the body of the PL-259.

OTHER SOLUTIONS

I have received further comments on this subject.

Richard Bown, G8JVM says "If you really must use PL-259 plugs, you don't need to solder the braid to the body of the plug.  Strip as normal but carefully fold the braid back over the outer PVC covering for the length of the connector, best also to use an extra long inner. Don't cut it to length first. Locate the inner conductor, then screw the cable into the connector clockwise. You may need to hold the PL-259 with large pliers when its in as far as it goes solder and trim the inner conductor, and if need be trim off any whiskers of the braid which are sticking out of the cable end of the plug. This makes a better connection of the plug as all the braid is in contact with the inner casing of the plug. This also works with Pope H100 type cable where the braid has been replaced with copper foil".

Walter Blanchard, G3JKV, notes "I agree with your piece re PL-259's. I gave up trying to solder through the  holes years ago and did what you do. I found if you fold RG-213-type braid back on itself - NOT over the black PVC covering - it is thick enough to provide a good grip for the plug's internal screw thread and you can screw the plug on right up to the end of the covering if you strip the right amount. If I think I might be taking the plug off again before long I don't solder the braid - just the inner - and that seems to do very well as long as it doesn't get wet. Soldering the outer braid can be a little tricky - some plugs don't take solder easily, and it has to be thin so the loose screwed attachment can slide back over it.

"Incidentally, there are PL-259s around that have a gold finish and are advertised as 'gold'. It's actually only a very thin plating and strips away easily from the muckite metal underneath so although it solders easily first time round the plating eventually gets pulled off by the solder and  the connection is lost.  Silver-plated PL-259s are far better if you can find them. PL-259s are much easier to assemble than N-type so I tend to use them for HF cables but stay with N for anything over 30 MHz".

I find that whether you fold the coax braid back over the black PVC covering or not may depend on the coax type and diameter and the PL-529 connector.

Brian Armstrong, G3EDD, adds "I felt I had to comment on your section on coax cable and UHF series connectors. Perhaps I should explain that although long since retired, I worked in the Engineering Department at Pye Telecom in Cambridge all my working life, and one of my responsibilities for many years was the approval of V/UHF aerials and the coaxial components that went with them. Firstly, UHF series connectors should never be used outside a protected environment, and those that are used should be with pressure sleeve clamp, which is much easier to terminate. We always used N series for all external applications, again with pressure sleeve clamp.

"I think that the UHF series is awful, but then they are cheap and everywhere. One of my ex-engineers, now retired, who is licensed, always changes the PL-529 series connectors on any equipment he buys for N or BNC series, a bit of a drastic step maybe and one that I have done myself but not on a regular basis."

PL-529 AVERSION

I find the aversion to the PL-529 rather difficult to understand. I have used them for years and have been unable to detect any deterioration in performance at HF compared with other types. I agree that at VHF and UHF it could be a different matter.  Much of the early home brew equipment used the cheap domestic TV coax connectors. Eric Knowles, G2XK, used to put out the best signal from Europe on 28MHz in the early 1960s using such connectors and television 75ohm coax.

The worst coaxial connector that I have ever come across is the old Pye clip-on type. In the RAF it was used to on coaxial connectors between units in airbourne RADAR installations and was the cause of most faults.