ZM2E will be operating from Quartz Hill (west of Wellington, New Zealand) from 31 March to 2 April.  Transmission will be 0.2 Hz frequency shift (137776/137776.2) and with dot length to suit conditions.  A beacon strategy has been agreed between participating stations, ZM2E will beacon with Z at FSK120 starting at 15 and 45 minutes past an hour, and other participants (all on unique frequency slots) will also beacon with FSK120 from the hour and half hour (see table for beacon ID short call sign).  If beaconing shows a path opens, then a QSO attempt will commence, in which case the beacon sequence lapses.  Dot length during QSO mode will be selected by each station, for what they think suits conditions, so there can be no advance notice of how third parties can best sticky beak on a QSO attempt.  At ZM2E we will have several PCs and run a range of Argo dot length displays, so we can handle anything that comes our way.

If ZM2E is not in QSO mode within an hour or so of Quartz Hill sunrise, then to facilitate possible reception reports from EU we will go to continuous beacon mode, sending ZZZ… at FSK120, and with timing of each Z starting on the hour and ten minute rests thereafter.

There is a bed and mattress firm in Wellington with a slogan: “You get more Zeds at Wellington beds.”  How that compares with ZM2E can be checked out from any listener reports.  We would hope that you get more Zeds from Quartz Hill, but the last laugh may be on us with the threat of watching eyelids during the third night.

There is no email at remote located Quartz Hill, but we will likely travel to town during the day to check email.

73, Bob ZL2CA (other ZM2E operators are Mike ZL4OL, David ZL4DP and possibly Con ZL2AFP)

Summary table of ZM2E LF DX aspirations for 31 March to 2 April 2007

| Station | Short call sign | DFCW frequencies | Grid square | Sunset | Sunrise | Path length to ZM2E |
| --- | --- | --- | --- | --- | --- | --- |
| VO1NA | V | 137776.9/137777 | GN37OR | 2155z | 0915z | 16246 km |
| VY1JA | J | 137778.1/137778.25 | CP20KW | 0345z | 1424z | 12227 km |
| ZM2E | Z | 137776/137776.2 | RE78IR | 0610z | 1841z | - |
| UA0AET | U | 137775.4/137775.6 | NO65KX | 1140z | 2330z | 13236 km |
| RX9BS | X | 137776.4/137776.6 | MO05UI | 1420z | 0130z | 15024 km |
| UA4WPF | W | 137777.0/137777.2 | LO66PU |  |  | 15559 km |
| RA3YO | Y | 137777.6/137777.8 | KO73DG | 1615z | 0325z | 16789 km |
| R6L | L | 137778/137778.2 | KN97LN | 1548z |  | 16480 km |

The current amateur world record distance for a 136 kHz two-way contact is 10311 km, between  ZM2E and UA0LE on 20 March 2004.