OPDS on 64bit machines

With the introduction of Windows 7 /8 64bit the era of 16-bit applications such as OPDS ended .
For the operation of OPDS or other older applications it is necessary to install a virtual machine XP32 . The freely available VMWare Player offers this possibility.
After the VMWare player installation, the client OS must be installed here . The requirements for memory and peripherals can be maintained (you can adjust later) . It is a normal XP installation (if used only for OPDS , you need to install only the necessary drivers).
Now for the configuration of the host system , only C:\spectum\Data\  had to be shared, thereby the access of OPDS provides data on the SpectumLab .
In client Explorer the file item Shared Files should now be visible. VMWare dubbed this folder by default as Z:  The \data folder should be seen here now. 
Now only the OPDS.ini needs to be adjusted :

sourcepath = Z:\data\
pattern = * . txt

myqth jo31jg = 'enter your 6- digit locator

fc = 137 550 ' nominal center for Op -32 ( Hz)
sr = 11999.9987712 ' calibrated sample rate (Hz )
dec = 25165824 '48 * 512k

' sr = 48000 ' alternative Speclab sample rate and decimation (Hz )
' dec = 113246208 '216 * 512k ( instead of 196 * Desired 512k)

' lorangri = 8000 6731 7499 ' active Loran Gris in central Europe : Russia Lessay Sylt
' lorantol = 0003 ' Eliminates Loran lines within + -3 MHz

reverse output = 1 'bottom -to -top
' uploadcmd = copy headline.txt + + DETECTED.TXT detecold.txt Z:\ public\detected.txt > nul
uploadcmd = Cleanup.bat 'copy results , then remove Remaining data files from Z:\data\

timetol = 2 ' assign multiple partial detections to same spot ( symbol durations )

' lower SNR thresholds for slightly more sensitivity :
' thresholddbcor = 14.5 ' default 15
' thresholddbc = 5 ' default 6

That was it. Now OPDS should work in conjunction with SpectrumLab .